## Slide 1
Performance & Ease-of-use
iconCFD
MESH & WRAP
Prepared by:
Mr. David Martineau
d.martineau@iconCFD.com
November 2016
With kind permission of:
Koenigsegg Automotive AB
Notes: Some important notes about using the template:
Don‘t touch the Master Slides! There is no need to.
Put the name of the meeting, your name, your contact email and date in the Title slide.
Title should be all caps. If it‘s necessary to use lower case, e.g. iconCFD, please highlight text, select font and deselect “all caps”.
To change the footer go insert header&footer and change footer for all slides apart from Title slides, not necessary to touch the Master slides.

## Slide 2: agenda
Introduction
Performance
Ease-of-use
Conclusions
iconCFD MESH & WRAP
Notes: To edit the agenda click on it. This will open the Text Pane. You can add / delete / modify agenda items here. Alternative is to click on the design tab and add the bullet points there. If you add bullet points these will be displayed in the microsoft default style. To apply ICON colours, select the shape, and edit the format of the shape. ICON colour is #7aa9cd (RGB 122, 169, 210). To highlight a special agenda item, simply set the other shapes to 75% transparency (right-click format shape).

## Slide 3: INTRODUCTION
iconCFD® WORKFLOW
iconCFD Process
  GUI
  MultiCase
iconCFD Wrap
iconCFD Mesh
iconCFD Cold
iconCFD Thermal
iconCFD Optimize
iconCFD VOF
iconCFD ... etc.
iconCFD Support & Documentation

## Slide 4: INTRODUCTION
iconCFD® MESH OVERVIEW
With kind permission of:
Koenigsegg Automotive AB
iconCFD® Mesh
Automatic hexahedral-dominant mesh generation
Creation of meshes with guaranteed quality on highly complex industrial models
Fully parallel meshing
with dynamic load
balancing
Support for multiple volume regions with conformal or arbitrary grid interfaces

## Slide 5: performance
hybrid parallelisation
Aims:
Reduce memory requirements
Exploit many-core cluster hardware
Future-proof the mesh generator for next generation HPC architecture
Objective:
Enable meshing using a combination of domain decomposition (inter-node) and multi-threading (intra-node)

## Slide 6: performance
hybrid parallelisation
MPI
MPI
MPI
process
process
process
process
MPI
process
process
process
process
MPI
process
process
process
process
MPI
process
process
process
process
MPI
Standard domain decomposition (no multi-threading)

## Slide 7: performance
hybrid parallelisation
MPI
process
thread
thread
process
thread
thread
MPI
process
thread
thread
process
thread
thread
MPI
process
thread
thread
process
thread
thread
MPI
process
thread
thread
process
thread
thread
MPI
MPI
MPI
Combined domain decomposition & multi-threading

## Slide 8: performance
hybrid parallelisation
process
thread
thread
thread
thread
process
thread
thread
thread
thread
process
thread
thread
thread
thread
process
thread
thread
thread
thread
MPI
MPI
MPI
Domain decomposition per node & multi-threading within node

## Slide 9: performance
hybrid parallelisation
Implementation:
Using “fork-join” multi-threading model
  Multi-threading can be added progressively
Added OpenMP directives to:
  All mesh quality checks
  Mesh topology relations
  Cell and face quantities (e.g. cell centre & cell volume calculations

## Slide 10: performance
hybrid parallelisation
Geometry courtesy of
Škoda Auto
Testing:
Mesh generated for industrial automotive case (Skoda Fabia II):
  30 million cells
Combination of domain decomposition & multi-threading on cluster:
  64 processes x 1 thread
  32 processes x 2 threads
  16 processes x 4 threads
  8 processes x 8 threads

## Slide 11: performance
hybrid parallelisation
Chart: Hybrid Parallelisation Performance
| 536.83000000000004 | 2999.46 | 2999.54 | 3011.38 | 3305.34 | 3305.34 | 3656.31 | 3656.31 | 3764.6 | 4028.02 | 6924.4 | 7460.45 | 7506.88
64 procs x 1 thread | 44.3881 | 133.779 | 133.779 | 132.948 | 136.077 | 136.077 | 138.47 | 138.47 | 135.266 | 132.292 | 139.751 | 135.712 | 135.301
32 procs x 2 threads | 24.8345 | 83.0573 | 83.0573 | 81.9971 | 88.9509 | 88.9509 | 94.4072 | 94.4072 | 85.8722 | 78.9829 | 93.1015 | 87.4454 | 86.5904
16 procs x 4 threads | 15.0096 | 63.6226 | 63.6226 | 63.9172 | 71.4551 | 71.4551 | 77.1003 | 77.1003 | 72.0708 | 64.9561 | 73.8747 | 68.7215 | 68.4377
8 procs x 8 threads | 10.0949 | 52.6786 | 52.6786 | 52.6509 | 60.5116 | 60.5116 | 65.8227 | 65.8227 | 60.3003 | 59.407 | 60.0655 | 52.0728 | 51.5298
Increasing number of threads per core:
reduces peak memory
increases runtime

## Slide 12: EASE-OF-USE
MOTIVATION
Geometry courtesy of
Škoda Auto
Major bottleneck in mesh generation:
  original CAD  watertight geometry representation
Translation of geometry from native CAD results in:
  Missing or duplicate parts
  Small gaps or overlaps
Resolving geometry issues
  Labour-intensive
  Time-consuming

## Slide 13: EASE-OF-USE
AIM
Integrated approach to wrapping and mesh generation
  Exploit existing adaptively-refined Cartesian grid generator
  Simultaneously perform wrapping and meshing
  Handle large gaps in model assemblies
  Avoid re-sampling geometry

## Slide 14: EASE-OF-USE
keep point
Geometry with gaps and refined mesh
Boundary faces (green)
Intersecting cells (red)
Cells connected to keep point (green)
Re-assignment of intersecting cells to keep region
Mesh corresponding to fluid domain
BACKGROUND
Process of identifying fluid region:

## Slide 15: EASE-OF-USE
Refinement level 1
Refinement level 2
Refinement level 3
COMBINED WRAPPING & MESHING
Current meshing process
  Tolerant of small gaps (geometry is wrapped at finest mesh level)
  Doesn’t handle large (fully-resolved) gaps
Solution:
  Perform wrapping at coarser refinement levels:

## Slide 16: RESULTS
Baseline mesh (no wrapping)
Result at wrap level = 3
Result at wrap level = 2
flange
Flange geometry from OpenFOAM® tutorial
Initial uniform Cartesian mesh created enclosing the geometry
The iconHexMesh mesh generator is then used to apply 4 levels of surface refinement

## Slide 17: RESULTS
flange
Wrapped surface with basic surface snapping
Wrapped surface with feature line snapping
Existing meshing functionality can be exploited to improve the capture of geometry features

## Slide 18: RESULTS
Gap faces (red) assigned to separate patch
Gap faces assigned to neighbouring patches
flange
Faces which close off holes in the geometry (gap faces) can be assigned to a separate patch or to neighbouring patches:

## Slide 19: RESULTS
Engine geometry:
887 separate components
42 million triangles
Wrapped surface:
Single closed manifold surface
762,028 triangles
engine block
Geometry courtesy of
Škoda Auto
Highly detailed engine block
Initial Cartesian mesh created with element size of 1.25m
Uniform surface refinement of level 9 applied to engine
  Small element size of 2.4mm
Wrap level of 5 applied
  Close holes < 40mm Ø
Wrapping process took 278s
  2 Intel Xeon X5650 (2.67GHz) processors

## Slide 20: RESULTS
engine block
Engine geometry
Wrapped surface
Wrapping is able to close large holes in geometry, whilst still capturing fine details:

## Slide 21: RESULTS
uhtm case
Geometry courtesy of
Škoda Auto
Detailed model of Skoda Fabia II including:
  electrical components
  exhaust system
  cooling
  power-train
  suspension
14 STL files:
  382 solids
  36 million triangles

## Slide 22: RESULTS
uhtm case
UHTM geometry:
36M triangles
Wrapped surface:
12.5M triangles
Geometry courtesy of
Škoda Auto
Initial Cartesian mesh created with element size of 0.625m
Surface mesh refined to level 8
  Element size of 2.44mm
2 levels of curvature refinement applied
Wrap level of 4
  40mm hole size
Complete process:
  Completed in 2h 42m
  32 cores with Intel Xeon E5-2670 (2.60GHz) processors

## Slide 23: RESULTS
UHTM CASE
Background mesh with no wrapping
Background mesh with wrapping activated
Geometry courtesy of
Škoda Auto

## Slide 24: iconCFD Mesh & Wrap
CONCLUSIONS
Domain decomposition and multi-threading can be effectively combined when meshing with iconCFD Mesh to fully exploit multi-core hardware architectures.
Wrapping functionality can be employed directly within the iconCFD mesh generation utility to handle poor quality input geometry without labour-intensive CAD repair, and without sacrificing geometry fidelity.

## Slide 25: ACKNOWLEDGEMENTS
The authors would like to thank Skoda for their kind permission to use the Fabia II vehicle geometry.

## Slide 26: Questions?
More information?
www.iconCFD.com
d.martineau@iconCFD.com

## Slide 28: Legal notices
This presentation is supplied in confidence, and commercial security on its contents must be maintained. It must not be used for any purpose other than for which it is supplied, nor may any information be disclosed to unauthorised persons. It must not redistributed, be reproduced in whole or in part without permission in writing from ICON.
And disclaimer
Please consider the environment before printing this presentation. We recommend ‘Greyscale‘ as printing color settings.
Notes: DO NOT DELETE THIS SLIDE. This needs to be in every slide show for legal compliance reasons.